## Slide 1
RA vs RCP
  Overview
8. January 2026
Tobias Belitz
HCTD/HCTS/HCTSN
Renesas Electronics Corporation
© 2026 Renesas Electronics Corporation. All rights reserved.
RENESAS CONFIDENTIAL

## Slide 2: Architecture Trend
The industry is experiencing significant transformation. Along with this, the E/E architecture will also change substantially. However, at this stage, we will focus only on two key changes related to data communication rather than covering all the modifications
Domain
Zone
Hybrid (Domain + Zone)
ADC
CDC
PT
CS
BD
Central GW
Central ECU
Zone ECU
PT
CS
BD
ADC
CDC
Central compute
PT
CS
ADC
CDC
Zone
BD
Central compute
ADC
CDC
Zone ECU
BD
VCU
PT
CS
Central compute
ADC
CDC
Zone
BD
Zone
PT
Zone
CS
Dev cost minimization
System BOM cost minimization
VC integrated type
VC centralized type
OR
OR

## Slide 3: Architecture type – tendency
Function centralization makes either zonal ECU to simplify or central compute to require higher performance
RT control
function
Service
application
I/O control
function
Sensor(s)
Actuator(s)
performance
VCU
Zone
Zone
Central compute
Zone
Zone
Zone+PT
Zone+CS
Central compute
Central compute
I/O
I/O
I/O
I/O
GbE
100MbE
CAN/LIN
Zone
Hybrid (Domain + Zone)
VC centralized type
PT/CS is reused from legacy so that required performance is not changed
Zone requires performance depends on actuator(s) connected to Zone
VCU merged several vehicle control functions requires higher performance than legacy
Zone requires performance depends on actuator(s) connected to Zone
Zone requires performance depends on vehicle function(s) or actuator(s) connected to Zone
All VC functions are integrated into central so that a powerful RT performance is required
I/O hub has only signal routing function and requires minimum performance
ADC
CDC
PT
Central ECU*
Zone
Zone
CS
*) In case of FOTA introduced
VC integrated type
OR
VCU: Vehicle Control Unit (incl. DCU), PT: Powertrain (xEV), CS: Chassis and Safety, BD: Body (BCM), ADC: ADAS Domain Controller, CDC: Cockpit Domain Controller, HPC: High Performance Compute
A: Increase of data routing
Routing Accelerator
B: IO Server
B: IO Control
Remote Control Protocol

## Slide 4: Routing vs Remote
The routing acceleration covers product’s network interfaces and accelerate communication between them. It provides forwarding and protocol conversions processing.
Edge Device
RCP Server
RCP Core
Eth Interface
SPI
I2C
MCU
Application
RCP Client
Sensor HAL (API)
Eth Interface
External Entities
RCP Clients communicate with Endpoints through RCP Servers using the Remote Control Protocol and also interact with external Entities connected to the Endpoints.

## Slide 5: Routing Accelerator vs RCP device
 | Routing Accelerator | Remote Control Protocol
Standard function | No; proprietary | Yes; OPEN Alliance
Function | Automated packaging (Un-) of data between CAN and Ethernet | Clint Server communication protocol, basically to control edge devices from the central compute unit
Packaging | IP (Soft macro) | Product (e.g MCU)
Data | Ethernet and CAN | Control of I2C, SPI, ADC, PWM etc. via Eth. frames
Location | Zone Controller | RC Clint  HPC RC Server Edge
Safety | Not covered; E2E protection if needed is not terminated by the RA, it is transparent routed | Covered; Edge node can add E2E protection to the Data
Security | MACsec, SecOC (TBD) | MACsec can be addon to the Ethernet communication

## Slide 6
Renesas.com
© 2025 Renesas Electronics Corporation. All rights reserved.
RENESAS CONFIDENTIAL